The Ohio State University

Department of Electrical and Computer Engineering

ECE 341

Autumn 2008

Mid Term – I

October 31, 2008

Name (print) ____________________________________________

Notice:

- There are 3 problems on the following pages.

- Please read the problems carefully.

- Draw circuit diagrams, show all the steps, and WINDOW THE FINAL ANSWERS.

### “No aid is given, received or observed”         Signature_____________

Grade_____________

Problem # 1:  (35 Points)

Consider a three-phase distribution feeder as shown below:

Compute the source voltage VS, if VR is to be maintained at 10 kV (line-to-line value)

Problem # 2: (30 points)

A three-phase Y-Y connected transformer is rated at 100 kVA, 69kV/13.2kV, and 10% short circuit reactance. This transformer supplies a load of 80 kVA at rated voltage, on the low voltage side, and 0.8 PF lagging. What is the voltage regulation of the transformer under these conditions?

Problem # 3: (35 points)

A 3-, connected transformer rated 138 kV/20 kV, 100 MVA, 10% short circuit reactance is loaded at its 150 percent of the transformer rating at p.f. 0.9 (leading). If the load voltage is set at 5% above the rated LV winding of the transformer; compute the:

- Source voltage

- Active and reactive power supplied by the source.