The Ohio State University

Department of Electrical and Computer Engineering

ECE 341

Autumn 2008

Optional Mid Term – I

November 24, 2008

Name (print) ____________________________________________

Notice:

- There are 3 problems on the following pages.

- Please read the problems carefully.

- Draw circuit diagrams, show all the steps, and WINDOW THE FINAL ANSWERS.

### “No aid is given, received or observed”         Signature_____________

Grade_____________

Problem # 1:  (40 Points)

Consider a three-phase feeder shown below:

The load bus voltage VR is maintained at 1.5 kV (line-to-line). Compute:

- Source voltage.

- Complex power supplied by the source.

Problem # 2: (30 points)

Consider a single-phase transformer rated 1.5kV/150V, 50 kVA. Assume that the low voltage side is short-circuited and the voltage, current and power measured on the high side is –

V= 20 V,    I=60 A, P= 36 W

- Determine the short-circuit impedance referred to the low voltage side.

- Determine per-unit value of the short-circuit impedance.

Problem # 3: (30 points)

A single-phase transformer is rated at 4 kVA, 440-V/220-V, 10% short circuit reactance. This transformer supplies a load of 2 kVA at rated voltage, on the low voltage side, and 0.9 PF lagging. What is the voltage regulation of the transformer under these conditions?