The Ohio State University

Department of Electrical and Computer Engineering

ECE 341

Autumn 2008

Quiz # 3

October 17, 2008

Name (print) ____________________________________________

Notice:

- There is one problem on the following pages.

- Please read the problem carefully.

- Draw circuit diagrams, show all the steps, and WINDOW THE FINAL ANSWERS.

### “No aid is given, received or observed”         Signature_____________

Grade_____________

Problem # 1:  (10 Points)

An ideal transformer (IT) rated 480V/ 220 V, 480 KVA is supplying a reactive load of 10 through a distribution line with reactance of 2. Assume the voltage at the primary winding of the transformer is set at 440 volts. Find the active and the reactive power supplied by the source.