The Ohio State University

Department of Electrical and Computer Engineering

ECE 341

Autumn 2008

Quiz # 4: Solution

Name (print) ____________________________________________

Notice:

§	There is one problem on the following pages.

§	Please read the problem carefully.

§	Draw circuit diagrams, show all the steps, and WINDOW THE FINAL ANSWERS.

“No aid is given, received or observed”         Signature_____________

Grade_____________

Problem # 1:  (10 Points)

A 100 KVA, 13.8 kV/440 –V single phase distribution transformer is tested on HV side with the following data:

Short Circuit Test:  Vsc=1200V, Isc=3.5A, Psc=800W

Determine the per-unit equivalent circuit of the transformer. Clearly denote the respective voltage bases on the per-unit circuit. Select Sb=100 KVA.