The Ohio State University

Department of Electrical and Computer Engineering

ECE 341

Autumn 2008

Quiz # 5

November 14, 2008

Name (print) ____________________________________________

Notice:

- There is one problem on the following pages.

- Please read the problem carefully.

- Draw circuit diagrams, show all the steps, and WINDOW THE FINAL ANSWERS.

### “No aid is given, received or observed”         Signature_____________

Grade_____________

Problem # 1:  (10 Points)

A 3-Φ synchronous generator rated 250-MVA, 13.8-kV, 10% reactance is connected to a load through a 3phase transformer rated 500-MVA, 13.8kV/138kV and 30% short circuit reactance. If the load is at fifty percent of the rating and p.f.=0.8 (leading) then answer the following questions.

Compute:

- If the load voltage is to be at rated value, compute the excitation voltage of this synchronous machine.  (6 points)

- What is the active and reactive power supplied by the generator. (4 points)

Select Vbase(at generator side)=13.8kV and Sbase=500 MVA