# EE 341 - Quiz #1

Name (please print): 	         Solution                The last four digits of your SSN:

1. A three phase 480-volt (line-to-line) system is connected to three phase loads. The first load consists of three light bulbs; each rated 120 Watts at 120 volts. The second load consists of three resistive heaters, each having 48-ohm resistance. Compute the currents in phase a, b, and c, and the total power supplied by the 480-volt system.

Solution:

a) Load 1:

so

and

Load 2:

b) Phase voltage

The single-phase equivalent circuit is as shown in the above figure.

c) ,

and ,

d)

or,

# Text boxes

### “No aid is given, received or observed”         Signature_____________

Rload2,Y

Rload1,Y

Ia

V(