# EE 341 - Quiz #2

Name (please print): 			              The last four digits of your SSN:

1. Consider a three-phase feeder shown below:

The load bus voltage VR is maintained at 1.386 kV (line-to-line). Compute the complex power supplied by the source and the power factor of the source.

# Text boxes

j1 (

Load #3:

180 kVA

p.f. = 0.0 leading

Load #2:

240 kW

p.f. = 0.8 lagging

Load #1:

300 kVA

p.f. = 0.9 lagging

Source bus

### “No aid is given, received or observed”         Signature_____________