# EE 341 - Quiz #4

Name (please print): 		Solution              The last four digits of your SSN:

1.   A 2.4 kVA, 240/120-V single phase transformer is tested on LV side with the following data:

Short-circuit test: V	A	W

The transformer is loaded at 50% of rated power with 0.8 PF lagging at rated voltage on the LV side. Compute the HV side voltage. (Hint: ignore excitation branch)

Solution:

(a)	Short-circuit test:

Equivalent impedance:

The equivalent circuit of the transformer referred to LV side is as shown:

(b)	LV side voltage:

LV side power:

LV side current:

HV side voltage (referred to LV side):

So the HV side voltage is

# Text boxes

### “No aid is given, received or observed”         Signature_____________