# EE 341 - Quiz #5

Name (please print): 			              The last four digits of your SSN:

1.   The following figure shows a power system consisting of a three-phase generator supplying a load through a transmission line with a pair of transformers at either end. If the load side voltage is to be kept at 480-V, compute the active and reactive power supplied by the generator.

# Text boxes

### “No aid is given, received or observed”         Signature_____________

480/13,800 V

1000 kVA

R=0.01 pu

X=0.04 pu

13,800/480 V

500 kVA

R=0.02 pu

X=0.085 pu

500 kVA

0.8 PF lagging