# EE 341 - Quiz #5

Name (please print): 		Solution              The last four digits of your SSN:

1.   The following figure shows a power system consisting of a three-phase generator supplying a load through a transmission line with a pair of transformers at either end. If the load side voltage is to be kept at 480-V, compute the active and reactive power supplied by the generator.

Solution:

This problem can be solved using per-unit system.

| Region 1 | Region 2 | Region 3 |
| --- | --- | --- |
| kVA | kVA | kVA |
| V | V | V |

Impedance of T2 needs to be transformed to new bases:

Load in per-unit:

Voltage at load side:

The per-unit equivalent circuit is as follows:

Load current:

Generator voltage:

Generator power in per-unit:

Actual generator power:

So, active power P = 424.5 kW, reactive power Q = 365.6 kvar.

# Text boxes

480/13,800 V

1000 kVA

R=0.01 pu

X=0.04 pu

13,800/480 V

500 kVA

R=0.02 pu

X=0.085 pu

500 kVA

0.8 PF lagging

### “No aid is given, received or observed”         Signature_____________