ECE 647

CODE COMPOSER TUTORIAL:

## Prepared by Sachin Puranik

### I. Introduction

Texas Instrument’s Code Composer StudioTM (CCS) is a user-friendly, Windows-based debugger for developing and debugging software for the TMS320LF2407.

It allows users to write and debug code in C or in TI assembly language.

Key Features:

- User-friendly Windows environment

- Ability to use code written in C and assembly

- Memory displays and on-the-fly editing capability

- Disassembly window for debugging

- Source level debugging that allows stepping through and setting breakpoints in original source code

- CPU register visibility and modification

- Real-time debugging with watch windows and continuous refresh

- Various single step/ step over/ step-into command icons

- Ability to display data in graph formats

- General Extension Language (GEL) capability that allows the user to create functions that extends the usefulness of CCSTM

II. Getting Acquainted with Code Composer StudioTM (CCS)

- How to - Open a Program, Build it and Load the Program onto the DSP.

- Turn on the Evaluation Module (EVM). - The green LED on the top right of the board will confirm that there is power to the board.

- Open Code Composer Studio by clicking “CC2000” icon from desktop.

- Go to the “Project” menu and select “Open” as shown in Figure 1.

Figure 1- Project Open Window

Open “realtime.mak”, which is found under - C:\tic2xx\c2000\tutorial\realtime.  (The project file is the master file that “holds” the other files together to build a working program)

- Once you have the project opened, look at the frame on the left side of the screen where “Files”, “GEL files” and “Project” are listed. Expand everything in the “Project” folder. When you are done, you should see the “Include” files, “Libraries”, and “Source” files as shown in Figure 2.

Figure 2- CCS Window with Opened Project

- The project file (*.mak) is the master file that links other necessary files together as a common filename. When you want to create a program with Code Composer, you will want to first create a new project, add a new source file(s) (*.asm or .c) to the project, add the linker command file (.cmd), and add “include” (*.i) or “header” (*.h) files.

- Now that you have the project opened, go to Option/Program Load, and check the “load program after build” box. This will automatically load the DSP compatible version of the program (*.out) file into the DSP after the build is complete.

Figure 3 – Program Load Options

- Now go to Project/Rebuild All. This will build and load the program into the DSP. If the program is being loaded onto the DSP, the disassembly window will open up automatically.

Note: It is recommended to RESET THE DSP each time you build or rebuild the project.

# How to – View the Disassembly

The disassembly window shows the assembly code that is stored in program memory. It also has a highlighted line that serves as the position marker when running the program.

To view the disassembly window as shown in the following figure if it is not already open, go to View/Dis-Assembly.

Figure 4 – Viewing Disassembly Window

# How to – View and Edit Memory Locations

The ability to view memory locations is vital to debugging. To view memory, go to View/ Memory. You should see a box pop up which will configure the memory window that is about to open (Fig 1.11). Please enter 0x300 for the start address.

Figure 5 – Viewing Memory Locations

Note: You can also change memory locations by double clicking on the memory location. A box will pop up that will allow you to enter in a new value. Double click on the 0x300 location in the memory window and change the value to 0x0555. The new value will appear in red signifying that the memory location has been changed.

# How to – View and Edit CPU registers

The CPU registers and CPU status registers are very helpful in debugging the code. To view these registers, go to View/CPU Registers (both registers are under this menu). Open both CPU registers. You should see the registers appear in new frames on the screen.

Note: You can also change CPU registers by double clicking on the registers. A box will pop up that will allow you to enter in a new value.

# How to – Open a Watch Window

In MAIN.ASM scroll down until you see the line “.bss Main_counter,1”. Highlight “Main_counter” and add that variable to the Watch Window.

A Watch Window allows us to view variables that we use in our code. Open a Watch Window by going to View/Watch Window.

You can add variables to this window by highlighting the variable name in the source code and then right clicking the mouse button and selecting “add to watch window”. To edit the display format of this variable in the watch window, double click on the variable name in the watch window. When the “edit variable” box appears, add the command “*(int*)” in front of the variable name. (fig 1.12) This configures the variable in the watch window to be displayed as an integer, thus ensuring that a decimal value is displayed. Otherwise, a hex value will be displayed.

# How to - Reset the DSP

Rebuild the project (that should also load the program as well) and reset the DSP by going to Debug Menu/Reset DSP.

# How to – Run/Halt the Program

Before you run any program, it is a good idea to make sure that no breakpoints have been set otherwise DSP will stop when it reaches the breakpoint.

To run the program, go to Debug/Run. Hitting F5 key can also run the program. (Observe as the value of “Main-counter” in the watch window changes).

To halt the program, go to Debug/Halt. Hitting Shift-F5 key can also halt the program.

# How to – Run the Program in Real-time Mode

Real-time mode is a useful feature of CCS that allows you to see changes as they happen but it is not necessary for program debugging. When CCS is not in real-time mode, the values in all windows will update as soon as program is halted or a break point occurs.

Real-time mode can be enabled as follows:

  - The DSP must have the program already loaded in order to enable real-time mode. (While in real-time mode, programs cannot be loaded to the DSP)

  - Reset the DSP by going to Debug Menu/Reset DSP.

  - Open the Command Window by going to Tools Menu/ Command Window.

  - Type in the Command Window “go MON_GO”.

  - Put CCS in Real-time mode by going to Debug Menu/Real-time Mode. When in real-time mode, you will see the word “REALTIME” in the bottom of the code composer screen.

  - Reset the DSP again and the program is ready to RUN.

Right click on the Watch Window and choose “Continuous Refresh”. This will allow the values in the Watch Window to change.

III. A Note on Source Level Debugging

Source level debugging lets you see where in the source code the program is running instead of having to decipher the disassembly window information. If a source code window opens up as well as the disassembly window when the project is built, Source Level Debugging is enabled. If not, you can enable the Source Level Debugging by going to Project/Options/Assembler Tab and checking the “enable source level debugging”. If you have just enabled Source Level Debugging, you need to rebuild the project before it takes effect.

### IV. A Note on User-defined Files, Linker Command Files and Source Files:

User defined files - “include” (*.i) and “header” (*.h)  are the files that are common to most programs. Functionally, both the files are same. Both types of files can define constants, macros (user defined callable functions), or variables.

The linker command file (*.cmd) is vital to the proper building of your code. It specifies where in the program memory to place sections of the program code, defines memory blocks, contains linker options, and names input files for the linker, names the (.out) etc. The linker command file also specifies memory allocations. Without a proper linker command file, CCS will not build the program properly. In our case, the linker command file is named ‘realtime.cmd’.

Source (*.c or *.asm) files contain the actual program that is to be run on the DSP. You must have at least one source file, but may have source files that call other source files. Be sure that all relevant source files are added to the project.

V. References:

- DSP-Based Electromechanical Motion Control by Toliyat and Campbell