Homework Set #8 (ECE743)

Problem 1:

The windings of the device shown in Fig. 1 are sinusoidally distributed, each with Ns equivalent turns. The bs winding may be arranged so that the bs axis is at an arbitrary angle ( with the as axis. Express ias and ibs so that mmfs has a constant amplitude and rotates in the counterclockwise direction regardless of the value of ( in particular,

.

Problem 2:

A two-phase induction motor is operating at a rated-load torque with balanced stator currents. The steady-state rotor speed is (r = 0.9(e. it is an eight-pole, 50 Hz device.

Determine the following:

- The actual rotor speed.

- The angular velocity of the rotor mmf relative to the rotor.

- The frequency of the rotor currents.

Problem 3:

Determine the actual no-load and full-load speeds ((rm) in revolutions per minute of the following device.

- A four-pole, three-phase 100 hp, 60 Hz, round-rotor synchronous machine.

- A 120-pole, three-phase 100 MW, 60 Hz, salient-pole synchronous machine.

- An eight-pole, two-phase 1 hp, reluctance machine supplied from a 5 Hz voltage source.

- A six-pole, three-phase 1/2 hp, permanent-magnet motor supplied from a 15 Hz voltage source.