Homework Set #9-1 (ECE743)

1. Problem 1: For a two-phase induction motor is assumed that Lls = L(lr = 0.001 H. The machine is supplied by a 110V, 60 Hz source, and has the following parameters:

rs = 0.4 (, r(r = 0.2 (, Irated = 30 A

How many times greater is the stall current larger than the rated current? Is this a problem?

2. Problem 2:

Consider a 2-phase, 8-pole AC induction machine. Derive an expression for the electromagnetic torque in terms of stator currents and rotor position in the stationary reference frame: ids, iqs, i(dr, i(qr, (r. Assume the following: Lss – stator inductance, L(rr – rotor inductance – mutual inductance.