Homework #1 (ECE743/Spring 2010)

1. Problem 1: For the magnetic system given below:

where: ly = 12 cm, lx = 4 cm, N1 = 400 turns, N2 = 800 turns, (0 = 4((10-7, (ry = 20000, (rx = 2000, Ax = 1 cm2, Ay = 1 cm2.

1). Determine the dot notation for both windings.

2). Compute L11, L12, and L22.

2. Problem 2:

Consider the elementary reluctance machine given below. Assume that the movable member rotates at an angular displacement ((r) and angular velocity ((r), respectively.

1). Derive an expression for the magnetizing inductance as a function of (r.

2). Write an expression for the flux linkage equation and voltage equation of the reluctance machine.