Homework #2 (ECE743/Spring 2010)

1. Problem 1:

An iron-core transformer which has two windings is shown below. N1 = 50 turns, N2 = 100 turns, and (r = 4000.

- Calculate L12, Lm1, and Lm2.

- Indicate the polarity of coupled coils with appropriate dots.

2. Problem 2:

Consider the elementary electromagnet shown below. Assume that the cross-sectional area of the stationary and movable member is the same and Ai = Ag = 4 cm2. Assume li = 20 cm, N = 500 turns, and (ri = 1000.

- Derive an expression for the magnetizing inductance Lm(x).

- Compute the value of the magnetizing inductance when x = 1mm.

3. Problem 3:

Express the force of attraction between the iron faces of the air gap for the figure shown below. Assume N = 1000 turns, g = 10-3 m and the switch “S” closes on the reactor when the input voltage V, is at its maximum value with the amplitude of 120 volts (f = 60 Hz). Neglect the reluctance of the iron. Assume rl = 1 ( and Ll = 0.01 H.