Simulation #2 (ECE743/Spring 2010)

1. Problem 1:

Consider the electromechanical system shown below:

where, g is the value of x at which the spring is at rest.

Assume that V is generated by a voltage source with the following waveform:

Assume that T = 0.001 for the trapezoidal voltage waveform and T = 0.001 when the input voltage is zero. Use the trapezoidal integration method with ( = 0.1 s.

Perform the following:

- Give the state-space equations for the above system.

- The trajectory and plot of V(t), x(t), dx/dt, i(t) and fem(t) with the trapezoidal input and x0 = g (the spring is at rest).

- The same as part b), except with no input and x0 = 0 (the spring is at maximum stretch).

# Text boxes

K = 2667 N/m

D = 10 Ns/m

N = 500 T

m = 0.8 kg

d = 1E-4 m

g = 3E-4 m

R = 10 (

A = 2E-4 m2

fext = 0