Simulation #2 (ECE743/Spring 2010)

Problem Statement: In this simulation a 2-phole, 2-phase 5hp, 110 V, 60Hz induction machine is to be studied. The machine’s parameters expressed in ohms are:

Short-circuited rotor

The reactances are expressed in 60Hz. The total inertia is J=0.026 kg.m2. At t=0 a set of rated voltages:

and

Are applied to the machine and the rotor accelerates from stall with no-load torque. Perform the following:

1)

a) Simulate the free acceleration characteristics in the stationary reference frame (i.e. iqs(t), ids(t), Te(T), ωr(t)).

b) Repeat part a for rotor reference frame.

2) Compute the steady-state value of  and the dynamic response of ia(t). Locate the peak value of ia(t) and then compute the ratio of . Discuss the significance of the.

3) Derive the steady-state equivalent circuit model for the machine. Use rotor reference frame. Show all steps.

4) Compute Ids and Iqs when the machine is loaded at 25% of its power rating for synchronously rotating reference frame.