Simulation #3 (ECE743/Spring 2010)

1. Problem 1:

Consider a permanent magnet dc motor. The rotor is initially at stall with TL = 0 and Bm = 6.04(10-6 N(m(s. the armature is stepped from zero to 6 V while the change in TL is zero. The motor is rated at 6 V, with the following parameters: ra = 7 (, LAA = 120 mH, kT = 2 oz(in/A, J = 150 (oz(in(s2. According to the motor data sheet, the no-load speed is approximately 3350r/min, and the no-load armature current is approximately 0.15 A. Determine the following:

where:

,,,.

- The transfer function between ia(s) and va(s). That is,

- The transfer function between (r(s) and va(s).

- The natural frequency of oscillation and damping factor.

- The state-space representation.

- Use Simulink and computer the time response of ia(t) and (r(t) when the armature is stepped zero to 6 V while the change in TL is zero.

- When the motor has reached its steady-state operation under part e), a load torque of 0.5 oz(in is applied. Compute the time response of ia(t) and (r(t).

2. Problem 2:

The field current of a dc shunt motor is held constant.

- Express the transfer function G(s) = i((s)/v((s) for no-load conditions.

- Show that if Bm = 0, this transfer function is identical in form to that of a series RLC circuit.

- Express R, L, and C in terms of machine parameters.