Simulation #4 (ECE743/Spring 2010)

Problem 1:

In this simulation, a 2-pole, 2-phase, 5 hp. 110 volts, 60 Hz induction machine is to be studied. The machine’s parameters expressed in ohms are:

rs = 0.295, Xms = 13.25,  Xls = 0.503, X(lr = 0.209, r(r = 0.144,

Br = 0.01 N(m(sec, Var = Vbr = 0 (short-circuited rotor)

The reactances are expressed at 60 Hz. The total inertia is J = 0.026 kg-m2. At t = 0, rated voltages, ,  are applied to the machine and the rotor accelerates from stall with no-load torque.

Perform the following:

- Simulate the free-accelerations characteristics in the stationary reference frame (i.e., iqs(t), ids(t), Te(t), and (r(t)).

- Compute the steady-state value of  and the dynamic response of ia(t). Locate the peak value of  ia(t) and then compute the ratio of . Discuss the significance of the .

- Derive the steady-state equivalent circuit model for the machine. Show all steps.