The Ohio State University

Department of Electrical and Computer Engineering

ECE 743

Spring 2010

Quiz #1: Solution

1.  How many state variables are necessary to describe the dynamics of the system shown in Figure 1?  - Ans:  4              (3 points)

Figure  1 - Electrical System

2. Write dynamic equations for the system shown in Figure 1.     (7 points)

From KVL in loop 1 (V, L1, R1, C1, V) :

,

From KVL in loop 2 (C1, L2, R2, L3, R3, C2, C1):

From KCL at the node in the middle:

,

From capacitance current formula:

In state space form:

where,

,   , ,