## Slide 1: Op-Amp Oscillator

## Slide 2: Here’s what you will build

## Slide 3: And here’s the schematic diagram
Each icon on the schematic represents an actual component

## Slide 4: We’ll see what each component is first
Then we’ll see how they work together to make the oscillator

## Slide 5: Each icon on the schematic represents an actual component

## Slide 6: Reading Schematics:
Battery
What’s this?

## Slide 7: Each icon on the schematic represents an actual component

## Slide 8: How about this?
Resistor
Current flowing through it creates a voltage

## Slide 9: Each icon on the schematic represents an actual component

## Slide 10: Capacitor
Store electrical energy in an electric field (static electricity).
Uses include:
  Timing circuits
  Coupling circuits
  Energy storage
  Bypass circuits
  Filter circuits
Eric Schrader
CC BY-SA 2.0

## Slide 11: Capacitors
Eric Schrader
CC BY-SA 2.0

## Slide 12: Each icon on the schematic represents an actual component

## Slide 13: Operational amplifier
Has two inputs
Function depends on circuit around it
  Highly versatile
We’ll use one
  It will function as a comparator

## Slide 14: Two come in one package
NOTE DIMPLE
Indicates pin numbering

## Slide 15: Comparator
Output depends on which input has a higher voltage
  If inverting input is higher, output is V-
  If non-inverting input is higher, output is V+

## Slide 16: Comparator
What will the output be?
4 V
2 V
+9V
-9V
?

## Slide 17: Comparator
What will the output be?
4 V
2 V
+9V
-9V
-9V

## Slide 18: Comparator
What will the output be?
4 V
6V
+9V
-9V
?

## Slide 19: Comparator
What will the output be?
4 V
6 V
+9V
-9V
+9V

## Slide 20: Each icon on the schematic represents an actual component

## Slide 21: What’s this?
Diode
  Lets current flow one direction but not the other
LED: current flow produces light
YES
X
NO

## Slide 22: Will current flow?

## Slide 23: How about here?

## Slide 24: And here?

## Slide 25: Each icon on the schematic represents an actual component

## Slide 26: “Ground”
We’ll use it as a reference point
Anything connected to ground is by definition at zero volts

## Slide 27: Quiz
0V
What is the voltage here?
It is 9V higher than ground
Ground is at 0 V
Thus this point is at +9 V

## Slide 28: Quiz
0V
What is the voltage here?
Ground is 9 V above this point
Ground is at 0 volts
Thus this point is at -9 V

## Slide 29: Let’s start with the voltage divider

## Slide 30: Remember the resistor
What is the voltage here?
It’s at ground
It’s at zero volts

## Slide 31: Remember the resistor
What is the voltage here?
It’s 9V above ground
It’s at +9V

## Slide 32: What do you think the voltage is here?
The arrow is halfway between +9V and 0 V
The voltage there is +4.5 V
How much resistance is above the arrow?

## Slide 33: How about now?
The arrow is 1/10th of the way up the resistor
How much resistance is below the arrow?
10 Ohms
What is the voltage at this point?
1/10th of 9V=0.9 V

## Slide 34: Kind of like a light dimmer switch
We can control the voltage by moving the lever, which Is just like moving the arrow

## Slide 35: If we don’t need to change it, we can just use two resistors

## Slide 36: If the output voltage is +9V
What is the voltage at the non-inverting input?
So about 1/2 of 9V

## Slide 37: Let’s review
What is the voltage on the non-inverting input?
  It’s +4.5 V
If the inverting input is at 5 V, what is the output?
  The output goes to -9V
If the inverting input is at -4 volts, what is the output?
  The output goes to +9V
47KΩ
47KΩ

## Slide 38: Notice our voltage divider is connected to the output!

## Slide 39: What is the non-inverting input voltage if the output is high?

## Slide 40: If the output is high, we have this
The non-inverting input is at +4.5 V
47KΩ
47KΩ

## Slide 41: What is the non-inverting input voltage if the output is low?

## Slide 42: Now the input is 1/2 of -9V
So the non-inverting input (the reference) changes with the output voltage
47KΩ
47KΩ

## Slide 43: Let’s look at the other input

## Slide 44: Suppose output is high
Remember a capacitor can store charge
Suppose there is no charge on it to start with
The instant you connect the battery, the capacitor starts to charge
  Current (electrons) flow to the capacitor and charge it up
  That takes time

## Slide 45: Here’s the voltage on the capacitor
It keeps charging until it reaches +9V
That’s as far as it can go
http://www.s-cool.co.uk/a-level/physics/capacitors/revise-it/charging-and-discharging

## Slide 46: But the output (of the op amp) could be at -9V!

## Slide 47: Now the capacitor wants to discharge
But it will discharge to –9V
http://www.s-cool.co.uk/a-level/physics/capacitors/revise-it/charging-and-discharging

## Slide 48: Whew! That’s a lot of stuff!
Let’s put it all together

## Slide 49: Suppose the starting conditions are:
Output is high
What is the voltage on the +input?
The capacitor has no charge (0 V)

## Slide 50: What is the output?
The output is at +9 V
The capacitor starts to charge
What happens when the capacitor voltage becomes greater than the non-inverting input?

## Slide 51: What will happen?
Right! The output will switch to low when the inverting input gets bigger than the non-inverting!
4.5V

## Slide 52: What will happen to the non-inverting input?
It will go to -4.5 V
4.5V
-4.5V

## Slide 53: Now which is higher, the inverting or non-inverting input?
The inverting!
So the output stays low
-4.5 V
+4.5 V

## Slide 54: Until the inverting input gets smaller than the non-inverting one
Then the output will go high again
But that means the non-inverting input also goes positive
Now the capacitor starts to charge up again
4.5V

## Slide 55: The process continues
4.5V

## Slide 56: How will we know if it’s working?
Add an LED at the output

## Slide 57: What’s this?
Diode
  Lets current flow one direction but not the other
LED: current flow produces light
YES
X
NO

## Slide 58: Will current flow?

## Slide 59: How about here?

## Slide 60: The breadboard

## Slide 61: The buses
Every hole along this green line is electrically connected

## Slide 62: There are four buses you can use

## Slide 63: All rows connected too

## Slide 64: Battery snaps first!

## Slide 65: Battery snaps first!

## Slide 66: Place chip in board
Dot or divot means up!
Note pin numbering scheme

## Slide 67: Connect negative supply

## Slide 68: Connect positive supply

## Slide 69: First resistor: 47K= yellow purple orange gold
Goes between pin 5 and 7

## Slide 70: Second resistor: 47K= yellow purple orange gold
Goes between pin 5 and ground

## Slide 71: Third resistor: 270= red purple brown gold
Goes between output and inverting input
Pins 6 and 7

## Slide 72: Capacitor
It has a plus and minus side!
One lead is shorter!
Short lead is minus!

## Slide 73: Capacitor
Short lead goes to ground
Long lead goes to inverting input

## Slide 74: It’s getting crowded
We still need to add this stuff
It also connects to output pin
Use a jumper wire to open up a new space

## Slide 75: Resistor for LED: 270 (red purple brown gold)
Connects from jumper to another node

## Slide 76: LED
It has a plus and minus side!
One lead is shorter!
Short lead is minus!

## Slide 77: Connect LED
SHORT LEAD GOES TO GROUND

## Slide 78: Connect the batteries!
270: red purple brown
47K: yellow purple orange
Capacitor: short lead goes to ground
LED: short lead goes to ground

## Slide 79: It should blink the light
Things to try:
  What would happen if you change the value of the feedback resistor R3? Try it.