## Slide 1: Pulse Detector
Ramiro Duarte, Clayton Greenbaum
Frank Paynter
Prof. Betty Lise Anderson

## Slide 2: Here’s what you’re going to build

## Slide 3: Principle of operation
An infrared beam passes through your finger
You are mostly transparent, but blood absorbs this wavelength
Amount of absorption depends on amount of blood
  Varies with your pulse
http://www.pulmolink.co.uk/products/pulse_oximeters/pulse-oximeter-work.html
Oximeters use two wavelengths, one for blood pulse and one for oxygen- we’ll use one to keep it simple

## Slide 4: First part is the sensor
Infrared light-emitting diode
Photodetector
Potato chip clip
Screw allows you to adjust the pressure
  Don’t want to squeeze the blood out of your finger!
LED
Photodiode

## Slide 5: Second is the part you’ll build

## Slide 6: Need to learn some things
How to read an electrical schematic
What parts we’re using
How to design the display
How to build the display

## Slide 7: Reading Schematics:
Battery
What’s this?

## Slide 8: How about this?
Resistor

## Slide 9: What’s this?
Diode
  Lets current flow one direction but not the other
LED: current flow produces light
Photodetector: should be hooked up backward (reverse bias)
YES
X
NO

## Slide 10: Will current flow?

## Slide 11: How about here?

## Slide 12: And here?

## Slide 13: Operational amplifier
Has two inputs
Function depends on circuit around it
  Highly versatile
We’ll use one
  It will function as a comparator

## Slide 14: Two come in one package
NOTE DIMPLE
Tells you pin numbering

## Slide 15: Comparator
Output depends on which input has a higher voltage
  If inverting input is higher, output is V-
  If non-inverting input is higher, output is V+

## Slide 16: Comparator
What will the output be?
4 V
2 V
+9V
-9V
?

## Slide 17: Comparator
What will the output be?
4 V
2 V
+9V
-9V
-9V

## Slide 18: Comparator
What will the output be?
4 V
6V
+9V
-9V
?

## Slide 19: Comparator
What will the output be?
4 V
6 V
+9V
-9V
+9V

## Slide 20: Ohm’s Law
V=IR
  Voltage equals current times resistance
  V = 1 ma X 1 KΩ
  V = ?
I = 1 ma

## Slide 21: Ohm’s Law
V=IR
  Voltage equals current times resistance
  V = 1 ma X 1 KΩ
  V = 0.001A X 1000Ω
  V = ?
I = 1 ma

## Slide 22: Ohm’s Law
V=IR
  Voltage equals current times resistance
  V = 1 ma X 1 KΩ
  V = 0.001A X 1000Ω
  V = 1 Volt
I = 1 ma

## Slide 23: Example: Sensor block
Current flows through LED
  Causes light
Light lands on photodetector
  Causes current
  Produces a voltage across R2
  Voltage will be input to next stage (filter)

## Slide 24: Output will look like
I
V
I
VOLTAGE
Ohm’s Law
V=IR
  Transforms the current signal into a voltage signal that the comparator can use

## Slide 25: DC Offset
VOLTAGE
DC Offset
~AC Signal
A fancy way of saying what voltage a signal is centered at

## Slide 26: DC Offset
Will be different for every finger

## Slide 27: Blocking Capacitor
Only AC signals can pass through a capacitor
  We can get rid of the DC offset so any finger will work in our circuit!

## Slide 28: Indicator Circuit
Compare the AC signal to 0V
Comparator drives indicator circuit
  When the signal dips below 0V, the indicator shuts off
  When the signal is above 0V, the indicator turns on
Signal
0V

## Slide 29: The breadboard

## Slide 30: The buses
Every hole along this green line is electrically connected

## Slide 31: There are four buses you can use

## Slide 32: All rows connected too

## Slide 33: Start by connecting supply
Connect negative (black wire) to one blue bus
Just stick the black wire in any hole on that bus
Connect red wire to the red bus
Disconnect battery from clip before proceeding

## Slide 34: Connect other negative bus
Connect a black wire from one blue bus to the other
Disconnect battery from clip before proceeding
Common Bus
Positive Bus
Negative Bus

## Slide 35: Place op amp on board
Check the divot!
Should be up!

## Slide 36: Which pins are the power pins?
Pin 8 goes to positive
Pin 4 goes to negative
Use the buses
Positive
Negative

## Slide 37: Connect op amp to power

## Slide 38: OK, we did POWER

## Slide 39: Now on to the sensor

## Slide 40: Here’s the sensor head
The one inside the clip is the PHOTODIODE
The one outside the clip is the INFRARED LED
We’ll connect the LED first

## Slide 41: Red is the ANODE
anode
cathode
positive bus
negative bus
anode
cathode

## Slide 42: Next, look at schematic
Need a resistor (R1) connected from the cathode of the LED to the common bus
  Cathode = pointy end of diode icon
  Resistor =100 Ω
  Stripes are brown, black, brown

## Slide 43: 100 = brown black brown
positive bus
anode
cathode
positive bus
negative bus
Ohm resistor connects LED cathode to negative bus
cathode

## Slide 44: Photodiode is upside down
Connect cathode to positive bus
Connect anode to a node
anode
cathode
anode
cathode

## Slide 45: Capacitor goes to pin 5
Positive
Negative

## Slide 46: Capacitor goes to pin 5

## Slide 47: 330K=orange orange yellow

## Slide 48: 1.5 M=brown green green

## Slide 49: 470K= yellow purple yellow

## Slide 50: We’ve done all this

## Slide 51: All that’s left is this!

## Slide 52: The LED has a long and short lead
Long lead is the Anode!
Short lead is the Cathode!

## Slide 53: Connect cathode to pin 7
cathode

## Slide 54: 330= orange orange brown

## Slide 55: To operate
Put clip on tip of finger
  If everything is working correctly, moving your finger in the clip should cause the LED to blink. If the LED never, ever blinks there is a problem with your circuit or one of the parts. (E.g. dead battery)
Adjust screw to make pressure gentle
Hold very still
Light should begin to blink with your pulse
  If you see a double blink with each pulse, you can move the clip to a thicker part of your finger (try a joint)

## Slide 56: Here’s what you’ve built
330