## Slide 1: Decisions in assembler code

## Slide 2: 3 < A < 8
Flowchart and assembler
  LDAA VALA
  CMPA #3
  BLE OUT
  CMPA #8
  BGE OUT
  Do action
  OUT continuation

## Slide 3: A<2 or A>=6
Flowchart and assembler
  LDAA vala
  CMPA #2
  BLT act
  CMPA #6
  BGE out
  act action for True
  out continuation

## Slide 4: 2<=A<=5
Flowchart and assembler
  LDAA vala
  CMPA #2
  BLT out
  CMPA #5
  BGT out
  action when true
  out continuation

## Slide 5: Simulation Assignment 1
Enter the following code into THRSIM
  ORG $50
  INNR RMB 1
  OTTR RMB 1
  ORG $E000
  LDAB #$FF
  STAB $1007 configure port C for output
  OL LDAA delayval try 1, try 10, etc
  STAA ottr
  TOP DECR INNR
  BNE TOP
  DEC OTTR
  BNE TOP
  EORB #$FF
  STAB $1003
  BRA OL
  LDA $FF
  END BRA END

## Slide 6: Sim Asg 1 (cont)
Before running your code configure an LED on pin PC 0. To do this go to the connect window, choose LED. When the popup comes up scroll in the left side and select PC0. Then hit connect. Then say OK.
After entering the code run your code, using different values for DELAYVAL
Note the difference in the time it takes from when you click on RUN until accumulator A becomes FF.
Try the program with delay val of 1 and delay val of $F0.
Change the value until you achieve approximately 1 second.

## Slide 7: Being able to reset simulator
If you want to be able to reset the simulator to rerun you code enter the following.
  ORG $FFFE
  FCB $E0
  FCB $00
What does this do? It resets the PC when a reset occurs to value $E000