Quiz 1

Consider the following problem statement:

The sequential circuit to be designed has a single input X and a single output Z.  The circuit will examine the input stream X once per clock.  When the sequence 011 is the last 3 inputs received the output Z will be set to 1 coincident with the last input of the sequence.  Z will be 0 otherwise.

Develop the state graph for the Mealy machine for this system.

It will help in grading if you include a table for the meaning of each state.

| State | Meaning |
| --- | --- |
| S0 | Have a non sequence 1 – on 1 stay in S0 – on 0 transition to S1 |
| S1 | Have the first 0 to start the sequence – on 0 stay in S1 – on 1 have 01 so far |
| S2 | Have the ending sequence 01 so far – on 0 back to S1 – on 1 have 011 and return to S0 |