Quiz 2

Write a VHDL ENTITY and ARCHITECTURE for a half adder.

A block diagram of the half adder is shown to the right.  A and Cin are inputs.  Sum and Cout are the outputs with

Sum = A xor Cin

Cout = A and Cin

Use TYPE bit for inputs and outputs.

THE VHDL ENTITY and ARCHITECTURE.

ENTITY halfadd IS

PORT (A, Cin : IN bit;

Sum,Cout : OUT bit);

END halfadd;

ARCHITECTURE one OF halfadd IS

BEGIN

Sum <= A xor Cin;

Cout <= A and Cin;

END one;