ModelSim overview

This is a non-graded assignment and a run through the ModelSim VHDL system.

The commands relevant to this VHDL system are: (on the Red Hat Systems)

vlib  library_name        this command creates a library for the analyzed designs.

(you will need a library called “work”)

vcom  design_file.vhdl  	the VHDL compile command

vcom   -source  design_file.vhdl     will print the source line and then the error message

vdel  design_unit   	deletes the design unit from the library

vsim			no arguments - starts up simulator - allows you to select library

and design unit.  The control window also allows you to compile

You can do everything from this window or use the specific

Commands.  You can even bring up a text editor to enter your VHDL.

vdir  [ -lib  <library_name> ]  [<entity_name>]   lists contents of a library

vmap  [<logical_name>]  [<path>]  defines a mapping between a logical library and a

library directory

qhmap   work   ~/ee762/pr_step2_lib

On the PC systems:

Under the FILE menu choose the Change Directory selection.  When the popup appears navigate to the directory where you will be doing the work for this course.

Under the FILE menu choose the Source Directory selection.  When the popup appears choose BROWSE and navigate to where your source files will be located.

The run through:

STEP 1)  In a terminal window on the Red Hat Systems do the following:

(--Bring up a terminal window.  NOT required on PC systems.)

Insure that you have a path set to access the mentor tools.  Execute

>echo $PATH

In response to this command you should get

PATH=/opt • • • with  /opt/local/mentormaster/modeltech/bin

somewhere in the path

>printenv | grep MGC

In response to this command you should get an appropriate response for your account.

If you do not get these (you may get more but that is ok), then add the following to your .login  file (at a point after the “setenv PATH ...”)

source    /opt/local/mentormaster/SETUP.MODELSIM

STEP 2)  Create a directory for your work in this class and possibly even subdirectories for this and one for the project steps.  Possibly ece762 and hw as the subdirectory.  Change directory to that directory and create a file with the following contents: (the remainder of this handout assumes you name the file,  hw1.vhdl)

You can use a text editor (be sure to save as plain text.  You can use the editor within ModelSim on both the PC and LINUX systems.  That insure the files are plain text.

ENTITY  first_test  IS

END  first_test;

ARCHITECTURE  one  OF  first_test  IS

SIGNAL  phi1, phi2 :  BIT;

BEGIN

PROCESS

BEGIN

WAIT FOR 10 NS;

phi1 <=  ’0’;	phi2 <= ’1’;

WAIT FOR 10 NS;

phi1 <=  ’1’;	phi2 <= ’0’;

END PROCESS;

END one;

The editor in the Modeltech GUI is under FILE- -> NEW - -> Source - ->VHDL

STEP 3)  In the directory for your work and contianing the file you just entered, you need to create a VHDL library.  To do this execute

-- start up the system

>vsim&        on LINUX systems or choose and click on PCs

Once MODELSIM is running

Under the file pulldown choose NEW(Library

A popup will ask for the Library name and the physical name – by default they are both “work”

Or from the command line you could have issued the command  (on LINUX)

>vlib    work

Then you can compile your design (this can also be done from the simulator window when you start it but try the command from the command line)

>vcom  hw1.vhdl

In the GUI choose COMPILE- -> COMPILE

A popup will allow you to choose hw1.vhdl  for compilation.

NOTE:  If you compile the unit from the command line it will not appear in library work until you (re)state the simulator.

STEP 4)  Now we want to simulate the design for 200 ns.

Using the “Simulate” pulldown, choose “Start Simulation”

Expand the + for “work” and choose the entity   first_test

Change the “Resolution” to  ns  (BE SURE TO DO THIS)

Unclick the optimization box.

Now click OK.

The VIEW or ADD pulldowns in the main window is used to activate the other windows.

The available windows are   Source, Structure, Variables, Processes, Signals, Wave, List

To see a waveform (or listing) for a signal,  activate the Objects window by clicking on “Objects” and then create a wave window.

View --> Wave . . .

You can add all the signals to the waveform (or list) using the Add pulldowns and the Wave and List in the choices  (With the “Objects” window highlighted)

Add ( Wave ( Signals in design

You will see the names of the signals added to the wave display.

(Within the Wave and List windows you can explicitly add a signal using the “Prop” pulldown.)

STEP 5)  You run the simulation using the RUN option of the Simulation pulldown.  You can change the value for how long the RUN selection is for in the Runtime Options.  You can also enter a command  RUN  200 ns at the command prompt in the transcript window of the GUI.

Run for 200 ns.  You should see the waveform generated in the Wave window.

STEP 6)  Open a list window       View --> List . . .    in main window

Add the signals              List --> Signals in design      in Signals Window

Save the listing to a file   File --> Write to File     in List window

STEP 7)  To print your listing results:  Highlight the list window – Under File choose “EXPORT(TABULAR LIST”         Name the file hw1.lst for example.

For the waveform use the “PRINT POSTSCRIPT” and print the results to a file which you can view and then print.  Be sure the waveform is a .bit or .pdf type file.

STEP 8)  Printouts.  You can print out the Listing and Wave results you created.

Review:  You can accomplish everything from the GUI window.

To create a new library the menu selection is on     File(New(Library…

(Note that you do want a library called work)

To create and edit a new source file of VHDL code it is   File(New(VHDL

(Note the simulator also works with Verilog and System C)

(This is actually a very nice editor for entering VHDL code)