ENTITY secs IS

PORT ( clk : IN BIT;

Reset_sec : IN BIT;

Secs : OUT BIT_VECTOR(5 downto 0) );

END secs;

ARCHITECTURE one OF secs IS

SIGNAL inext_sec, isec : BIT_VECTOR(5 downto 0);

SIGNAL incrnext_sec : BIT_VECTOR(5 downto 0);

SIGNAL incr_sec_carry : BIT_VECTOR(6 downto 0) := “0000001”;

BEGIN

-- F/F process

PROCESS

BEGIN

WAIT UNTIL (clk = ‘1’ and clk’event);

isec <= inext_sec;

END PROCESS:

--Next State

-- First the next seconds count

-- Have   inext_sec = isec+1

incrnext_sec <= isec xor incr_sec_carry(5 downto 0);

incr_sec_carry(6 downto 1) <= isec AND incr_sec_carry(5 downto 0);

--The rest of the next state logic

PROCESS

BEGIN

IF (reset = ‘0  or  incrnext_sec = “111100’)

THEN inext_sec <= “000000”;

ELSE

inext_sec <= incrnext_sec;

END IF:

END PROCESS:

--THERE may or may not be further output logic

--Here you would want to go from the 6 bit representation to 2 bcd

--You have to at least do the following

Secs <= isec;

END one;