## Slide 1: A package for fault testing
ECE 764 – Project B

## Slide 2: Outline
Why is package needed?
What is package to do?
The verification task.

## Slide 3: Why is package needed
In modern circuits, as we push to reduce gate length and operating voltages, errors are becoming more prevelant.
In the 1970s and 1980s fault simulators were a focus of VLSI research. These fault simulators allowed simulation of circuits in response to stuck-at and intermittent faults.
VHDL, Verilog, and System C HDL systems do not currently support fault simulation.
COULD THEY?

## Slide 4: HDL Fault Simulation
The languages could support fault simulation.
A package for fault_simulation_logic could be created much like std_logic_1164
The standard functions, such as AND, could be overloaded.
In fact, all the functions would be overloaded.
Each time the function is evaluated, a probability function is called. In most cases the correct result is returned, but when the value returned from a probability function is above a threshold, an erroneous result is generated.

## Slide 5: For example
In 1164 have
FUNCTION “and” (l : std_logic, r : std_logic) RETURN UXO1 IS BEGIN
RETURN (and_table(l,r));
END “and”;

## Slide 6: For this package would have
Fault_simulation_logic
FUNCTION “and” (l : fsim_logic, r : fsim_logic) RETURN fsim_logic is
VARIBLE rtnval : fsim_logic;
BEGIN
IF prob() < limit
THEN rtnval <= fsim_and_tbl(l,r);
ELSIF prob() < 0.5 THEN rtnval <= ‘0’;
ELSE rtnval <= ‘1’;
-- or maybe error values also come from the table
END IF;
RETURN(rtnval);
END;

## Slide 7: The assignment Proj B
Create the package for overloading the functions and generating the appropriate probability distribution function. (will have to reference some papers on fault simulation and fault simulators for which distribution function to use)
Test the package on several “simple” designs to insure that errors are being injected.
The intent is to be provided with a medium level of complexity unit with many gates (calls to the error function) for evaluation of the package.
Will set values of the probability of an error occurring to a value where you do not have to simulate days for this to happen.

## Slide 8: The steps in Proj B
Proj B test plan
  Plan and timeline the project – 3 weeks –
  List and assign the tasks to a team member
Proj B report
  Report on the testing of the package on several test circuits
  The test circuits will be provided but will require modification to the signal type names your design uses.