## Slide 1: Build a speaker

## Slide 2: Sound wave
Compressional wave
Air is compressed and expanded rhythmically
Created by something vibrating
blog.modernmechanix.com

## Slide 3: A speaker vibrates
The paper diaphragm vibrates
Pushes the air
The sound waves travel to your ear
Tiny hairs in your ear wave in the breeze
Your nerves pick this up, detect as sound
www.physclips.unsw.edu.au/ jw/electricmotors.html

## Slide 4: How do we make the sound?
We must convince the paper to vibrate in synch with our music
Our music is generated by our (stereo, mp3player, etc.) as an electrical signal
High frequency electrical signal=high frequency sound
  Low=Low
  Music is a combination of lots of frequencies
www.cs.dartmouth.edu/ ~dwagn/aiproj/speech.html

## Slide 5: We will use electromagnetism
We will create a force field:
We will make an electric field
  That creates a magnetic field
    That creates a force
The force will push the paper

## Slide 6: First, think about magnets
Like poles repel
  South repels south
Opposite poles attract
The magnets produce a force
http://www.swe.org/iac/lp/magnets_03.html

## Slide 7: We say the magnet has a field
The field is invisible
But it is real
It can act on objects
Repel or attract them

## Slide 8: Example: compass needle
Opposite poles attract
North end of compass needle attracted to south pole of magnet
Why can’t we feel the magnetic field?
hyperphysics.phy-astr.gsu.edu/.../ elemag.html
  We’re not magnetic!

## Slide 9: Let’s Practice
Web.mit.edu/
Physics 8.02
Module Guide 09
Which side is the N pole?
Which side is the S pole?

## Slide 10: Let’s Practice
Web.mit.edu/
Physics 8.02
Module Guide 09
Solution:
Arrows point out of the North pole and into the south pole.

## Slide 11: Let’s Practice
Web.mit.edu/
Physics 8.02
Module Guide 09
Will these magnets attract or repel each other?

## Slide 12: Let’s Practice
Web.mit.edu/
Physics 8.02
Module Guide 09
Opposite poles attract:

## Slide 13: Let’s Practice
Web.mit.edu/
Physics 8.02
Module Guide 09
We can even make the magnets oscillate! (vibrate)

## Slide 14: So we can push magnets around
Big whoop. We want to push the paper around.
  Paper is not magnetic.
  What should we do?

## Slide 15: So we can push magnets around
Big whoop. We want to push the paper around.
  Paper is not magnetic.
  What should we do?
Glue a magnet to the paper

## Slide 16: Then what?
We want to push the magnet around, but in synch with our music
Our music is in the form of an electrical signal right now
We will put electromagnetism to work

## Slide 17: First piece of information
When current (I) flows though a wire, it creates a magnetic field (B)
Use right hand rule to find direction
http://en.wikipedia.org/wiki/Electromagnet

## Slide 18: Is this drawn correctly?
Web.mit.edu/
Physics 8.02
Module Guide 09

## Slide 19: If the current changes
Suppose the current reverses direction
What will happen to the field?

## Slide 20: If the current changes
Suppose the current reverses direction
What will happen to the field?
  It will reverse
Can we use this to push a magnet around?
  Yes, but it’s pretty weak

## Slide 21: Suppose we make a loop
All the field lines inside the loop go the same direction
  Is the figure drawn correctly?
The field gets concentrated
physicsed.buffalostate.edu/.../ rhr/rhr.htm

## Slide 22: Remember Two Magnets?
Web.mit.edu/
Physics 8.02
Module Guide 09
Will these magnets attract or repel each other?

## Slide 23: Remember Two Magnets?
Web.mit.edu/
Physics 8.02
Module Guide 09
Will these magnets attract or repel each other?

## Slide 24: Replace one magnet
Web.mit.edu/
Physics 8.02
Module Guide 09

## Slide 25: Reverse Current
Web.mit.edu/
Physics 8.02
Module Guide 09

## Slide 26: Electricity creates oscillation!
Web.mit.edu/
Physics 8.02
Module Guide 09
By alternating the current direction…
We can make the coil oscillate!

## Slide 27: Ok! We can push the magnet!
But the field is still weak.
Need a way to amplify the field.

## Slide 28: A bunch of loops=electromagnet
www.utm.edu/~cerkal/ magnetic.htm

## Slide 29: OK, we have all the pieces!
Need a paper diaphragm
Need a “voice coil”
  About 50 turns should do it
Need a magnet
And a music source!
  (and probably an amplifier)

## Slide 30: Voice coil
Slide straw over dowel
Wrap wire around straw
  Leave about 6” free before you start winding
  Leave 6” at the end
Overlap wire as much as possible
  Make sure all wire is on the straw
Twist wire so it doesn’t unwind
When finished, slide coil to one end of straw
Remove dowel

## Slide 31: Burn speaker leads
Burn 1 inch of the end of each of the two wires coming off the coil.

## Slide 32: Diaphragm
Cut out template
Cut slot at white line
Make cone and tape it

## Slide 33: Glue magnets to the square

## Slide 34: Attach coil to diaphragm
Glue long end of straw to bottom of cone
  Coil should be at end away from cone
Don’t get glue on the end of the straw away from the cone – need room for magnet to move!

## Slide 35: Tape legs to the cardboard
Coil should hover above or gently rest on cardboard after all four legs have been taped.

## Slide 36: Connect to audio cable
Twist yellow wire and one lead from your speaker together
Twist red or white wire with other speaker lead.

## Slide 37: Tape audio cable to cardboard
Tape the black audio cable to the edge of your cardboard.

## Slide 38: Position Magnets Inside Coil
Do not tape paper down! (Yet)

## Slide 39: Once it works, tape the square

## Slide 40: Connect to mp3 and play!
You have applied electromagnetism to create sound from an electrical signal.
How do you suppose a microphone works?

## Slide 41: Troubleshooting
Volume set to max?
Speaker is plugged into phone all the way?
Magnets are inside the coil?
Coil can easily slide up and down on the magnets?
Coil is at the bottom of the straw? (Closest to the cardboard)
1 inch of each speaker lead was burned?
The two twisted connections are not touching each other?
If your audio cable doesn’t have a red, white and yellow wire, you can use any two wires
Try re-twisting the audio cable to the speaker leads!